## Slide 1: SSPayWMN: Secure and Seamless Prepayment for Wireless Mesh Networks
Can Serhat Leloğlu
canleloglu@sabanciuniv.edu
Thesis Presentation as of January 18, 2013

## Slide 2: Outline
Thesis description
Building blocks of the system
Protocol specifications
Simulations of SSPayWMN
Discussion on success of SSPayWMN
Conclusions

## Slide 3: Thesis in a Nutshell
A secure prepaid payment scheme for broadband Internet access is designed and developed in a simulation environment.
This scheme will be particularly for Wireless Mesh Networks with multiple operators.
Proposed scheme provides privacy and untraceability.
System performance is evaluated using network simulations.

## Slide 4: Objectives
Wide coverage
Seamless Roaming
Seamless Mobility (Handoff)
Anonymity
Mutual Authentication
Two-way honesty
Untraceability
Performance

## Slide 5: Differences and Similarities with an Earlier Work

## Slide 6: System Entities
 | Mobile user (client)
 | Access Point (AP) with mesh routing capability. From now on in this document, it is called as AP, but please note that it also has routing capability.
 | Mesh backbone of the operator
 | Gateway (GW) that connects the mesh backbone to outer world and also to the operator's server
 | Operator's server (OP). Keeps necessary logs and user info.
 | Trusted Third Party (TTP). Payment related logs are mostly to be generated by the TTP.

## Slide 7: Building Blocks
Connection Cards
Hash tokens
Aliases
Generation Order
Spending Order

## Slide 8: Initial Authorization and Reuse of a Connection Card

## Slide 9: Access Point Authentication
In order to authenticate the network by the client

## Slide 10: Packet Transfer
After mutual authentication of client and access point, client starts to send data packets to access point.

## Slide 11: Changing Alias

## Slide 12: Disconnection

## Slide 13: Seamless Mobility in Home Operator
When a client moves out of the coverage area of its associated AP or if another AP provides a better service, the client may want to hand off to another AP.

## Slide 14: Seamless Roaming
When the clients need to get service from an access point of a new operator, they roam between old operator and new one.

## Slide 15: Performance Evaluation of SSPayWMN
The simulations of SSPayWMN are conducted using ns-3.
The simulator was run on a computer with 2.4 GHz Intel Core 2 Duo, 2 GB 1067 MHz DDR3, Apple MacBook OSX v10.6.8.

## Slide 16: Simulation Environment
The network topology is hierarchical and WMN supports connections with other IEEE 802.11 protocols, clients communicate with TTP via access points, GWs and operators in sequence.
Access point specifications are given below.
AP-Gateway Connection bit rate | 6-54 Mbps – Wi-Fi
AP-Gateway Distance | 70 m
Service Duration per token | 5 minutes
Update Interval | 11 minutes

## Slide 17: SSPayWMN Simulations
We have conducted the simulations of SSPayWMN in two groups.
Unit Tests: Independent protocol runs to analyze the delay caused by protocols.
Real-life Scenario Simulation: These simulations evaluate the system’s overall performance in an ordinary day usage with client mobility and realistic Internet service demand.

## Slide 18: Unit Test Results
Unit Test Result for End-to-end Two-Way Protocols

## Slide 19: Unit Test Results
Unit Test Results for Access Point Authentication

## Slide 20: Unit Test Results
Unit Test Result for Seamless Mobility and Roaming

## Slide 21: Unit Test Results
Unit Test Result for Packet Transfer

## Slide 22: Client Types
Three different user types are outlined with different networking and mobility requirements.
  Students
  Employees
  Domestics

## Slide 23: User Modeling and Mobility in Real-Life Scenario
The proposed system intends to serve a variety of users.
Clients perform certain kinds of actions and all of these actions are triggered as a result of a random event.
 | Morning | Daytime | Evening
Domestics | 0,40 | 0,60 | 0,60
Students | 0,20 | 0,20 | 0,80
Employees | 0,20 | 0,99 | 0,20
 | Morning | Daytime | Evening
Domestics | 0,90 | 0,98 | 0,80
Students | 0,30 | 0,20 | 0,98
Employees | 0,30 | 0,99 | 0,20
Become Active
Probabilities
Stay Active
Probabilities

## Slide 24: User Actions
In real-life scenario simulations, network usage related actions are modeled using two-state Markov Chain.

## Slide 25: Mobility
Clients move on a grid, to reach a randomly selected destination. The speed and the distance to destination differ according to client’s type.

## Slide 26: Simulation Results of Protocols
Real-Life Scenario Simulation Result for Initial Authorization Protocol

## Slide 27: Simulation Results of Protocols
Real-Life Scenario Simulation Result for Reuse of a Connection Card Protocol

## Slide 28: Simulation Results of Protocols
Real-Life Scenario Simulation Result for Changing Alias

## Slide 29: Simulation Results of Protocols
Real-Life Scenario Simulation Result for Disconnection

## Slide 30: Simulation Results of Protocols
Real-Life Scenario Simulation Result for Seamless Mobility in Home Operator Protocol

## Slide 31: Simulation Results of Protocols
Real-Life Scenario Simulation Result for Roaming Protocol

## Slide 32: Simulation Results of Protocols
Real-Life Scenario Simulation Result for Packet Transfer

## Slide 33: Overall Burden of the System

## Slide 34: Discussion
Wide Coverage
Seamless Mobility and Roaming
Anonymity
Mutual authentication
Two-way honesty
Untraceability
Performance

## Slide 35: Conclusion
SSPayWMN is a secure and seamless prepayment scheme, which provides privacy and untraceability for the clients.
This system provides fairness to both operators and to clients.
Seamless mobility and roaming
Unit test simulations and real-life scenario simulation results ensures the system’s stability and steady state performance.

## Slide 36: Thank you
Very much