## Slide 1: Usage of Hash Chains
Can Serhat Leloğlu

## Slide 2: Initial Authorization & Reuse-CC
In the authentication phase, the client guesses the number of tokens that he is going to use before the next Alias change
  For 5 minutes of hash token renewal interval
  For 50 minutes of change alias interval
  The sum of tokens before the next Change Alias protocol is:
    50 / 5 = 10
Client forms up an alternative hash chain of 10 tokens related to the original hash chain

## Slide 3: Generation of Alternative Hash Chains
H0
H1
H2
H3
H4
H5
H6
H7
H8
H9
H10
H11
H12
H13
Original Hash
Chain
H0’
H1’
H2’
H3’
H4’
H5’
H6’
H7’
H8’
H9’
H10’
H10’ = h(H10 ⊕ Nonce)
Client sends H0 to TTP, client and TTP calculate the alternative hash chain in Initial Authorization or Reuse-CC protocols
TTP calculates the Alias and last token of the alternative hash chain (e.g. H10’) by using the same nonce value
Client uses the hash tokens in the alternative hash chain to get service
If the client disconnects before spending all of the alternative hash tokens (e.g. At H3), the next time he connects; he will generate a new alternative hash chain starting from the last point (e.g. H3 to H13).
Anonymized Sub-Hash
Chain

## Slide 4: Change Alias
Every 50 minutes access points broadcast Change Alias commands
Access points prolong the service intervals of existing aliases by 1 minute to make the change alias process seamless to the clients.
Clients use the new alternative hash chain to get service once their 1 additional minute is over

## Slide 5: Seamless Mobility and Roaming
Seamless Mobility and Roaming protocols transfer current hash token from one access point to another
The transfered hash token will be the current hash token that client uses from the alternative hash chain
The protocols will not change at all

## Slide 6: Discussion
This scheme adds some tiny delay to the system (Less than 0.08 second)
The transmitted packet lengths are the same with the previous proposition
  The network simulations will not change drastically
There is no reverse connection between original and alternative hash chains
  The actions of the clients are indeed untraceable between sessions